## Slide 1: Zedboard Booting
Creation of bin files and images through petalinux
by
S Vishnu vardhan reddy

## Slide 2: Petalinux Installer
Installed petalinux installer version 2024.1
Open the folder which you want to install
It helps to install the petalinux with the simple command line on terminal i.e path/to/installer ./petalinux-v2024.1-05202009-installer.run
Asks some approval for licenses, accepts all.
Shows “PetaLinux SDK has been successfully set up and is ready to be used” and create some files in the folder.

## Slide 3: Setting petalinux environment
Command source settings.sh
It sets up the necessary environment variables and paths required for building and working with PetaLinux projects.
After command execution it sets PetaLinux environment to the current folder and ready to build projects.

## Slide 4: Project creation
Petalinux-create is the command used in this step.
Command line petalinux-create project --template zynq --name ZEDBOARD is used to create a new project.
‘Project’ in the command line define this is the type project, --template defines the board family and --name defines the project name.
The above command create a new folder with a name ZEDBOARD(which is the name of project) within the current folder.

## Slide 5: Configuration
Using the xsa.file (which is designed in vivado and contains hardware details) petalinux config the hardware.
Using the command “petalinux-config --get-hw-description /path/to/the/xsa.file/ZEDB OARD.xsa”
‘--get-hw-description’ gets the design and hardware details of the board in the xsa file
Petalinux-config configure the details to the current project.
Configure the appropriate machine name in DTG settings, ‘zedboard’ here .
After the execution of command in second step, petalinux open a window in the terminal for user to check and adjust the details manually (if required).
Optionally we can configure our root file system if we need to through command “petalinux-config -c rootfs” .

## Slide 6: Building project
After configuring the requirements that user need, the next step is building the project.
Through the command “petalinux-build” the building process takes place.
Proper internet connection and space is required for building the project without errors.
To build project in offline mode it is necessary to download the PetaLinux Tools sstate-cache Artifacts of the appropriate petalinux version for the appropriate board.
Try to build once again if faces TIMEOUT ERROR.
Building process requires more space (upto 40GB) and time, based on the board and manual configuration of the board.
If the project built successfully it shows up “Successfully built project”.

## Slide 7: BIN File Generation
It's time to generate the bin file, which is essential for the booting process.
Command “petalinux-package --boot --u-boot” generates the BIN file file, which is formed from combining the files zynq_fsbl.elf, u-boot.elf and system.dtb.
Now all the required files are ready to boot the zedboard.

## Slide 8: SD Card Formatting
We have to format SD card properly in-order to use in the booting process.
It can be done in either terminal or the application called ‘gparted'.
“ls /dev” list out the device files(linux assumes every device as a file ) in the system.
Unmount the all partitions of SD card and format the SD card using commands “umount /dev/<sd card device file name > and sudo fdisk /dev/mmcblk0”.

## Slide 9: SD Card partition
After executing the above command it opens a special space on the terminal.
Character ‘p’ used to list out the details of sd card, ‘n’ used to create new partition, selects the primary partition and number, define size less than 5GB for partition-1 and for second partition it takes all free space as default.
Type ‘y’ to remove vfat signature.
Change types of partitions to FAT32 and Linux(ext4) for partition -1 and partition-2 respectively using characters ‘t’ and ‘l’ ( l lists the types of filesystems ).
“ sudo mkfs.msdos /dev/mmcblk0p1 and sudo mkfs.ext4 /dev/mmcblk0p2” commands can also be used to configure filesystems.

## Slide 10
6. For labeling the partitions the commands “ sudo fatlabel /dev/mmcblk0p1 name-1 and sudo e2label /dev/mmcblk0p2 name-2 ” are used respectively for partitions 1 and 2.
7. Note
Remember to type hex number of filesystem after typing character t.
All this process can be done through gparted application also.

## Slide 11: File Transfer
Transfer the files BOOT.BIN,boot.scr and image.ub to the first partition of the SD card which is formatted by FAT32 file system.
Unzip the rootfs.cpio or rootfs.tar.gz file with appropriate command into the second partition of the sd card through using terminal.

## Slide 12: Booting on Zedboard
Place the SD card into the card reader of the Zedboard.
Connect Zedboard to the pc using USB to micro-usb cable.
Open the application gtkterm or minicom in the pc.
Connect the power supply to the Zedboard.
Set up the Jumpers to sd card mode i.e jp11 - jp7 with 01100.
Power on the Zedboard and set appropriate configuration on the gtkterm, those are like port, baud rate, number of parity bit and etc.
Observe the output on the console.

## Slide 13: Thank You