## Slide 1: DMA DRIVER
MICRO DMA
by
S Vishnu vardhan reddy

## Slide 2: PROJECT MOTO
Design a simple and efficient Linux device driver that seamlessly interacts with axi-dma while allowing user to configure.
Develop a user-friendly application that complements the driver, which provide flexibility and safety in configuring dma.

## Slide 3: DRIVER DESIGNING
Driver design includes three main components which further divides into individual modules.
  Initializing mechanisms
    Handles driver registration, probing, removal, reset and other essential setup functions.
  Userspace Interaction Mechanism
    Implements file operations to build communication between the driver and application.
    open , read, write, poll and close are the functions used.
  DMA Interaction mechanisms

## Slide 4: APPLICATION DESIGNING
The application is designed to enable safe and efficient user interaction with hardware. It is divided into two key components:
DDR Interaction Mechanism
  Utilizes the default memory driver via the mmap() call to interact with DDR memory.
  Provides the capability to read and write to any memory region safely.
DMA Driver Interaction
  Enables reading DMA register values, including both MM2S (Memory-to-Stream) and S2MM (Stream-to-Memory) channels simultaneously.
  Provides individual functions to configure different DMA registers for specific purposes, including:
    Starting and stopping DMA
    Resetting DMA
    Configuring source and destination addresses
    Setting transfer length
    Error checking and handling

## Slide 5: DMA INTERACTION MECHANISM ( Driver)
Manages AXI-DMA register space for efficient DMA operations.
  Manages AXI-DMA register space for efficient DMA operations.
  DMA Run/Stop/Reset Module: Controls DMA operation states.
  Independent Function Modules: Enables users to configure S2MM (Stream-to-Memory) and MM2S (Memory-to-Stream) channel registers independently via user-space application calls.
  Transfer Configuration & Control: Manages AXI-DMA transfers between memory and peripherals.
  Polling Mechanism: Checks and updates the transfer status to the user-space application.
  Error Handling Module: Identifies and reports specific error conditions during failures.
  Interconnected Modules: For example, the polling function is executed after every DMA channel operation to monitor status effectively.

## Slide 6: SAFETY MECHANISMS IMPLEMENTED
Restricted Direct Address Inputs
  Prevents users from providing direct address inputs, avoiding improper register handling and unintended hardware access.
Flexible Input Handling
  Supports both decimal and hexadecimal input formats, enhancing usability.
Error Handling & Input Buffer Management
  Clears the input buffer after every invalid input to prevent unintended operations and ensure smooth execution.
Resilient Data Retrieval
  The driver retrieves data in multiple formats, allowing continued functionality even in case of user-space failures.
Comprehensive Error Checking
  Dedicated error functions verify the correctness of every operation, ensuring system stability and debugging support.

## Slide 7: TESTING
Both the driver and application were tested with various test cases and performed as expected.
There is scope for optimization, particularly in improving performance and reducing overhead.

## Slide 8: DEBUGGING NOTES
DMA Transfer Length Limitation
  Ensure that the length does not exceed: Burst Length×(Memory Mapped Data Width8)\text{Burst Length} \times \left(\frac{\text{Memory Mapped Data Width}}{8}\right)Burst Length×(8Memory Mapped Data Width​)
  Exceeding this limit can cause improper DMA transactions.
Micro DMA Mode Configuration
  The XSA design must enable Micro DMA mode in AXI-DMA to ensure proper operation.
Memory Accessibility Check
  Verify that AXI-DMA has access to the required memory space before initiating a transfer to avoid access violations.

## Slide 9: —------THANKS—------