## Slide 1: AXI-DMA
Scatter-Gather Mode
by
S Vishnu vardhan reddy

## Slide 2: PROJECT MOTO
Design a simple and efficient Linux device driver that seamlessly interacts with axi-dma in scatter gather mode, while allowing user to configure.
Develop a user-friendly application that complements the driver, which provide flexibility and safety in configuring dma.

## Slide 3: DRIVER DESIGNING
Driver design includes Four main components which further divides into individual modules.
  Initializing mechanisms
    Handles driver registration, probing, removal, reset and other essential setup functions.
  Userspace Interaction Mechanism
    Implements file operations to build communication between the driver and application.
    open , read, write, poll, ioctl and close are the functions used.
  DMA Interaction mechanisms
  BD mechanisms

## Slide 4: APPLICATION DESIGNING
Memory Interaction
  Memory Access via mmap(): Leverages the default memory driver to map DDR memory into user space, enabling direct and secure access. ​
  Read and Write Capabilities: Allows users to perform read and write operations on specified memory regions, ensuring data integrity and safety.​
  Binary File Loading: Supports loading binary files into user-defined memory locations.
DMA Driver Interaction
  Register Access: Provides simultaneous reading of DMA register values for both MM2S (Memory-to-Stream) and S2MM (Stream-to-Memory) channels.​
  Control Functions: Includes functionalities to start, stop, reset the DMA, configure source and destination addresses, set transfer lengths, and perform error checking for both channels, ensuring robust control over DMA processes.​
  Buffer Descriptor Management: Incorporates a dedicated section for handling buffer descriptor operations, optimizing data transfer efficiency and management.​

## Slide 5: DMA INTERACTION MECHANISM ( Driver)
Manages AXI-DMA register space for efficient DMA operations.
  Manages AXI-DMA register space for efficient DMA operations.
  DMA Run/Stop/Reset Module: Controls DMA operation states.
  Independent Function Modules: Enables users to configure S2MM (Stream-to-Memory) and MM2S (Memory-to-Stream) channel registers independently via user-space application calls.
  Transfer Configuration & Control: Manages AXI-DMA transfers between memory and peripherals.
  Polling Mechanism: Checks and updates the transfer status to the user-space application.
  Error Handling Module: Identifies and reports specific error conditions during failures.
  Interconnected Modules: For example, the polling function is executed after every DMA channel operation to monitor status effectively.

## Slide 6: BD MECHANISM ( Driver)
This component is dedicated to the efficient handling of buffer descriptors for user-specified channels, ensuring seamless data transfer and control.
Dynamic Buffer Descriptor Allocation:
  Enables users to create a specified number of buffer descriptors tailored to their channel requirements, offering flexibility in resource management.​
Exclusive Use of ioctl Calls:
  Facilitates robust communication between user-space applications and this management module through the exclusive use of ioctl system calls.
Buffer Descriptor Management:
  Provides functionalities to set and clear values within buffer descriptor registers.

## Slide 7: SAFETY MECHANISMS IMPLEMENTED
Restricted Direct Address Inputs
  Prevents users from providing direct address inputs, avoiding improper register handling and unintended hardware access.
Flexible Input Handling
  Supports both decimal and hexadecimal input formats, enhancing usability.
Error Handling & Input Buffer Management
  Clears the input buffer after every invalid input to prevent unintended operations and ensure smooth execution.
Resilient Data Retrieval
  The driver retrieves data in multiple formats, allowing continued functionality even in case of user-space failures.
Comprehensive Error Checking
  Dedicated error functions verify the correctness of every operation, ensuring system stability and debugging support.

## Slide 8: TESTING
Both the driver and application were tested with various test cases and performed as expected.
There is scope for optimization, particularly in improving performance and reducing overhead.

## Slide 9: DEBUGGING NOTES
DMA Transfer Length Limitation
  Ensure that the length does not exceed: Burst Length×(Memory Mapped Data Width8)\text{Burst Length} \times \left(\frac{\text{Memory Mapped Data Width}}{8}\right)Burst Length×(8Memory Mapped Data Width​)
  Exceeding this limit can cause improper DMA transactions.
SG Mode Configuration
  The XSA design must enable SG mode in AXI-DMA to ensure proper operation.
Memory Accessibility Check
  Verify that AXI-DMA has access to the required memory space before initiating a transfer to avoid access violations.

## Slide 10: —------THANKS------—