## Slide 1: Booting Process
.;ljkl/l/l/l.
by
S Vishnu vardhan reddy

## Slide 2: BOOT ROM
It is a program which was dumped by the vendor during manufacturing.
This is stored on a non-volatile memory which is embedded on the board.
Executes first at power on or reset.
Main purpose is determine the boot mode through boot pins, search and load the BOOT.BIN file into ram from FAT partition of SD card or any other peripheral memory.
Performs basic H/W checks for essentials like cpu and memory etc.

## Slide 3: BOOT.BIN
This is the file that we created through prtalinux using xsa.file
It consists FSBL, Bitstream, ATU, PMUFW and in some cases u-boot also.
It loads the FSBL.

## Slide 4: FSBL(First stage boot loader)
FSBL setup the hardware using bitstream and initialize the most of the hardware components.
FSBL is a small interms of size so it does’nt have capability to load the kernel.
Intialises the Arm Trusted Firmware (ATF) and load Platform Management Unit Firmware (PMUFW) which controls the power, clock and thermal conditions of the system.
After setting environment, FSBL loads the U-boot into the ram and transfer the control.

## Slide 5: U-boot
U-boot using boot.scr file which is located in SD card, search for the system.dtb which is also on SD card.
U-Boot passes the device tree information to the Linux kernel. This is done by providing the address of the .dtb file in memory to the kernel via the boot parameters.
boot.scr file provide commands to do the operations for u-boot.
Using the same boot.scr file u-boot determine the location of image.ub which is the image of kernel and os.
After setting the environment, U-boot loads the Kernel into the SRAM or DDR.

## Slide 6: Kernel
After kernel loaded into the ram it take over the control of system and starts initializing.
It uses the system.dtb file to configure and initialize appropriate drivers & hardware devices respectively.
Using initrd which is a minimal file system, kernel set up and initialize the essential drivers and environment.
Which extremely required to initialize the all device drivers, core code and kernel modules using complete root filesystem.

## Slide 7: System services
Later system services starts one by one.
The first service is the init service whereas later login service, email service, network service and so on initialize.
From there, user can operate or use the system.

## Slide 8: Thank you