## Slide 1: Universal Serial Bus (USB) Deep Dive
Beginner to Advanced Overview
Vishnu All In One

## Slide 2: What Is USB and Why It Matters
Standard interface for connecting peripherals to hosts
Goals: simplified cabling, hot‑plug, USB‑powered devices, scalable speeds
Speeds from 1.5 Mb/s (USB 1.0) to 10 Gb/s (USB 3.1)

## Slide 3: Quick History of USB
USB 1.0 (1996): Low‑Speed (1.5 Mb/s), Full‑Speed (12 Mb/s)
USB 1.1 (1998): Minor clarifications
USB 2.0 (2000): High‑Speed (480 Mb/s)
USB 3.0 (2008): SuperSpeed (5 Gb/s), USB 3.1 (2013): 10 Gb/s

## Slide 4: USB Topology & Enumeration
Tiered‑star: Host → hubs → up to 127 devices
Host controllers: UHCI/OHCI/EHCI/xHCI
Enumeration: descriptors → address assignment → driver load

## Slide 5: Physical Layer & Signaling
USB 2.0 cable: VBUS, GND, D+, D– twisted pair
Differential NRZI encoding + bit‑stuffing for clock sync
Signaling states: J‑state, K‑state, SE0, SE1

## Slide 6: Transfer Types & Endpoints
Control, Interrupt, Bulk, Isochronous transfer types
Endpoints: unidirectional channels (EP 0 is bidirectional)
Max packet sizes vary by speed and transfer type

## Slide 7: Packet & Frame Structure
Frames: 1 ms (LS/FS), 125 µs microframes (HS)
Transactions: Token → optional Data → optional Handshake
Tokens: IN, OUT, SETUP, SOF; Handshakes: ACK, NAK, STALL

## Slide 8: USB Descriptors Deep Dive
Device, Configuration, Interface, Endpoint, String descriptors
Optional: BOS, Device Qualifier, IAD, class‑specific
Descriptors form a hierarchical tree

## Slide 9: USB On‑The‑Go (OTG)
Dual‑role devices: host or peripheral
ID pin in Mini/Micro‑AB connectors
Protocols: SRP (Session Request), HNP (Host Negotiation)

## Slide 10: USB 3.0 SuperSpeed Highlights
Three differential pairs: legacy + TX/RX SuperSpeed
8b/10b encoding, up to 5 Gb/s raw
Layered protocol: Physical, Link, End‑to‑end

## Slide 11: Linux USB Software Stack
usbcore: API for control, bulk, interrupt, isochronous
Host Controller Drivers: UHCI/OHCI/EHCI/xHCI
Class drivers and Gadget framework (device‑side)

## Slide 12: USB Enumeration in Software
Hub status URB signals attach event
Control URBs: GET_DESCRIPTOR, SET_ADDRESS, SET_CONFIGURATION
Process completed in microseconds

## Slide 13: URBs & Data Movement
URB lifecycle: allocate, fill, submit, complete, free
usb_anchor groups URBs for bulk cancel on disconnect
Callbacks handle completion and errors

## Slide 14: Descriptor Usage in Code
MODULE_DEVICE_TABLE matches VID/PID or class
usb_get_descriptor & control URBs fetch descriptors
Parsing usb_host_config, interfaces, and endpoint descriptors

## Slide 15: Mass Storage Class (Host Side)
Bulk-Only Transport: CBW → DATA → CSW sequence
wraps SCSI commands in USB bulk URBs
Interfaces scsi_cmnd with block layer

## Slide 16: HID Class (Host Side)
Interrupt URB on IN endpoint polled at bInterval
hid-core parses report descriptor → input events
Applications read /dev/input/eventX

## Slide 17: Key Kernel Data Structures
struct urb: central USB transfer descriptor
struct usb_anchor: groups URBs for cancellation
Completion API: usb_complete_t callbacks

## Slide 18: Device Classes in Code
hid_driver: probe(), disconnect(), input layer integration
usb_storage_driver: SCSI host template, probe, block layer
Gadget drivers: composite framework with functions